CW OSC/AF AMP/2 TONE OSC - Rev B

This module includes the above three circuits. CW is transmitted by keying the crystal controlled oscillator at about 9000.3 kHz. A relay controlled by the 12vCW supply from the controller board determines whether a DSB or CW signal is passed on to the post mixer/pre-driver board.

TR1 turns on the voltage to the oscillator when keyed and also provides a voltage to the VOX circuit on the transmit exciter board which switches the transceiver to transmit whenever the key is pressed.

The AF amplifier uses the TDA2003, a 10W car radio audio amplifier, preceded by a single transistor amplifier. The IC is fitted with a heat sink. The input is taken from the DBM on the transmit exciter board via J2. If the Transmit Exciter control board is used, then the two outside pins on J1 should be shorted.

The two tone oscillator is used in TUNE mode, the supply voltage being obtained from the controller board. The balance control is adjusted to produce two equal tones about 1 kHz apart and is best set with an oscilloscope. The level should be adjusted so that peaks are equal to the peaks produced by your microphone in normal speech. It can be used to tune up linear amplifiers and ATUs (if you must) and monitoring the wave form will indicate linearity (or lack of it)

COMPONENTS LIST

Resistors  0.25W

  - R27		R7  =  wire link

4.75			R26

- R10

- R3

- R25,28

- R48

- R47

- R39

- R11

- R20

- R12

- R2

1k5			R1,5,12

1k8			R46

3k3			R43

5k6			R22

6k8			R8,42

10k			R13,14,19

12k			R9

15k			R4

22k			R36

47k			R44

100k			R21,37,40,41

330k			R38,45

Resistors preset horizontal

1k			VR1

100k			VR2

Capacitors

1n   multi layer ceramic	C28,29

10n multi layer ceramic	C2,3,5,6,10,13,14

100n multi layer ceramic	C16,24,40

220n multi layer ceramic	C11,26

10pF	ceramic plate		C7

220pF 	ceramic plate		C8,9

0.033   Mylar			C41,42

0.10	Mylar			C35,36

100uF 25v electrolytic		C25

470uF 25v electrolytic		C27

1uF 16v tantalum bead	C1,4,37,43

2.2uF 16v tantalum bead	C17,18,34

10uF 16v Tantalum bead	C19,20,23,38,39,44

Trimmer capacitors			Inductors

3/30pF				C12	Toko 10RBH	150mH	L1,2

Type 43 ferrite bead	FB1

Thermistor

1k				TH1

Semiconductors

2N2222A			TR5

2N3563			TR2,3

2N3904			TR4

2N4402			TR1

BC182L			TR7,8,9

1N4148			D1,2,3

TDA2003			U1

Crystal

Nom 9000 kHz HC18U 30pF		X1

Relay

SPCO 12v OMRON G5V-1		RLY1