COMPONENTS LIST – FRONT END BOARD		REV B	BPFLIST.doc

Capacitors

100n	multi layer ceramic				C79,80,119,120,142,171,173,106

220n	multi layer ceramic				C74,75,76

470n	multi layer ceramic				C77

2p7	ceramic plate					C159,160,161

3p3	ceramic plate					C156,157,158

3p9	ceramic plate					C165,166,167

4p7	ceramic plate					C162,163,164,168,169,170

5p6	ceramic plate					C90,107A,117,99

15p	polystyrene					C86,88,91,101,102,105,109,118

18p	polystyrene					C82,83

22p	polystyrene					C46B,49,52B,53B,59B,61,63,65

27p	polystyrene					C54,56,47,51,58

33p	polystyrene					C40,42,44

39p	polystyrene					C41B,43B,60A,60B,66A,66B

47p	polystyrene					C11B,17B,33,35,37,48B,50B

56p	polystyrene					C32B,38B,39A,45A

68p	polystyrene					C26,28,30,39B,45B,53A,59A,94,98,111,115

82p	polystyrene					C3,46A,52A

100p	polystyrene					C18A,19,21,23,24A,32A,38A,95,112

120p	polystyrene					C89,92,93,96,97,100,107,108,110,113,114,116

150p	polystyrene				C12A,12B,14A,14B,16A,16B,34B,36B,85,87,103,104

180p	polystyrene					C4B,10B

220p	polystyrene					C18B,24B,31,62,64

270p	polystyrene					C5B,7B,9B,48A,50A,55,57

330p	polystyrene				C5A,7A,9A27A,27B,29A,29B,34A,36A,41A,43A,81,84

390p	polystyrene					C20B,22B,25

560p	polystyrene					C11A,17A,20A,22A,70

680p	polystyrene					C1,2

1000p	polystyrene					C4A,10A

1800p	polystyrene					C6A,6B,8A,8B,13,15

10000p polystyrene					C78

22uF 16v tantalum					C43,69,73

Capacitors surface mount Y5V multi layer ceramic 50v

100n							C68,71,140,141

10n							C121-129

1n							C130 - 138

Resistors

0.125W metal film 1% MF12 series

10k					R20,21,22,23,24,25,26,27,28,29,30,31,32,33,34,35,36,37

0.25W metal film 1% MF25 series

51R							R12,13,14,15

56R							R8

220R							Rx1

1k							R9

10k							R10,39,16,38

22k							R11

82k							R6,7

Resistors surface mount 1206 0.125W 1%

2k2							R4,5

Resistors surface mount 0805 0.1W 1%

39R							R45

82R							R42,44

100R							R41

150R							R46,48

10k							R17

Semiconductors

Integrated Circuits

74AC74						U1

ULN2803						U3,5

FST3125						U2

PCF8574						U4,6

Voltage regulators

# REG1

LM317							REG2

Inductors (except BPF)

16t 0.315mm enam on T50-10 toroid			L31

17t 0.315mm enam on T50-10 toroid			L30

17t bifilar 0.315mm enam on T50-10 toroid		L32/33,36/37

31t 0.315mm enam on T37-6 toroid			L34,35,38,39

6t 0.315mm enam on ferrite bead			FB1,2

Mini-Circuits TT4-1A RF transformer			T1,2,3

0.82uH axial choke					RFC1,2,3,4,5,6,7,8,9

1uH axial choke					RFC10

Relays

SPCO	5v OMRON G5V-1				RLY3,4,5,6,7,8,9,10,11,12,13,14,15,16,17

18,19,20

SPCO 12v OMRON G5V-1				RLY1,21

DPCO	12v (Farnell 310-3500)			RLY2,2A

Crystals

9MHz Parallel resonant in 30pF by C-MAC ref A164A		X1,2,3,4,5,6,7,8

(Sterling Components, Slough. Phone 01753 779000)

Available from G3OGQ at £2.00 each plus £1.00 postage.

Connectors

IDC 10 pin						J2

Inductors for band pass filters

Ref		TOKO ref				Lodestone Pacific*			Ind

L1		E526HNA1000076			5T 0.4MM ON L45-10-PCT-B-4	0.22uH

L2		KXNSK4173AO			20T 0.2MM ON L45-6-PCT-B-4	3.52uH

L3,4,5		KANSK4960EG			39T LITZ ON L45-2-PCT-B-4		15uH

L6,7,8		BKANS9440HM			29T 0.2MM ON L45-2-PCT-B-4	8.2Uh

L9,10,11	BTKANS9443HM			25T 0.2MM ON L45-6-PCT-B-4	5.6uH

L12		BTKANS9443HM			22T 0.2MM ON L45-6-PCT-B-4	4.8uH

L13,14		154ANST10052			21T 0.2MM ON L45-6-PCT-B-4	4.3Uh

L15,16,17	KXNSK4173AO			18T 0.25MM ON L45-6-PCT-B-4	2.8Uh

L18,19,20	KANS12354BM2			16T 0.25MM ON L45-6-PCT-B-4	2.4Uh

L21,22,23	KANS12354BM2			15T 0.25MM ON L45-10-PCT-B-4	2.1Uh

L24,25,26	BTKANS9449HM			14T 0.25MM ON L45-10-PCT-B-4	1.5Uh

L27,28,29	KXNSK4172EK			12T 0.315MM ON L45-10-PCT-B-4	 1.3uH

*www.lodestonepacific.com. These coil formers offer a considerable improvement in performance over Toko. There is little difference in cost.