# COMPONENTS LIST – SYNTHESISER Rev B				synthlist.doc

Capacitors

1n	multi layer ceramic		C43

100n    multi layer ceramic		C2, 8,13,16,17, 21, 27, 28, 55, 56, 57, 58,69

220n	multi layer ceramic		C3

47p	ceramic plate			C15

100n	polyester			C24

1uF	polyester			C23

1n5	polystyrene			C18

2n7	polystyrene			C19

1uF 16v tantalum			C6

10uF 16v tantalum			C5,7,25,63

10uf  35v tantalum                             C4

22uF 16v tantalum			C20,22,26,62

100uF 16v tantalum			C14,29,37

220uF 16v tantalum			C1,68

470uF 16v tantalum			C12

Capacitors surface mount 0805 NPO (COG)

3p3					C34

10p					C32,45,47

15p					C42

18p					C33,46

47p					C31,44

1n					C35

10n					C38,39,40,41,49,50,51,52,53,66

# Capacitors surface mount Y5V multi layer ceramic 50v

100n					C10,11,36,54,59,60,61

# Resistors 0.25W metal film 1% MF25 series

100R					R42

470R					R29,32,33,37

590R					R1

1K					R53

4K7					R31,34

9K1					R2

10K					R52

15K					R28

68K					R35

100K					R54

220K					R30

1M					R36,40

# Resistors surface mount 0805 0.063W 1%

100R					R43,44

270R					R49,50

470R					R51

1K					R57,58,60

2K2					R45,46,47,48

4K7					R55,58

# Resistors surface mount 0805 0.1% 10ppm/C

7k5 (Farnell 554 844)				R16,17,18,19,20,21,22,23,24,25,26,27

15k (Farnell 555 137)				R4,5,6,7,8,9,10,11,12,13,14,15

# Resistors SIL pack

100k						R41A - E

# Inductors

470uH axial DC res 4 ohms max		RFC3,4,7

1mH axial DC res 4 ohms max		RFC5

5 turns 0.315 enam on FB			RFC1,2,6,12,13,14

6u8 SMC Farnell 200 542			RFC8,9

22uH SMC Farnell 200 578			RFC10,11

TOKO A700 9550W custom			L1,2

(limited supplies available from G3OGQ, price £1.20 each)

# Semi Conductors

# Integrated circuits

74HCT9046 (Quarndon)			IC5

HSP45102PC-33*					IC2

PCF8574					IC9

74AC00					IC11

74AC163					IC10

74AC74					IC7

74AC86					IC6

74HC174					IC3,4

74HC393					IC8

32 MHz crystal oscillator

(Farnell 221 685)				X1

*NOTE: The HSP45102PC-33 is no longer manufactured. If you cannot get this version, we recommend the surface mount version HSP45102SC-33 or 40 with adapters SOIC to 28pin DIP (e.g. Farnell 547 268 and 233 134). SC-40 is available from G3OGQ at £17 .

# Diodes

BA782 (superceded by BA582 - supplies available

from G3OGQ, price £6.40 per set)		D4,5,6,7,8,9,10,11

BB619 (superceded by BB639 - supplies available

from G3OGQ, price £1.50 per set) (Electrovalue)		D2,3

1N4148					D12

4V7 0.25W Zener				D1

# Transistors and FET

J310						TR5,6,7

2N3904					TR1,2,4

2N3906					TR3

MMUN2215LT1 SOT23 digital

(Farnell 473 625)				TR8,9

# Voltage Regulators

- REG2

7808						REG1

LM217LZ					REG3

# Sundries

3 Pin header					J3

10 Way IDC header				J1,2

Screening Box Eddystone 11451P

(with M3.5 x 16 long screws)			1 Off