COMPONENTS LIST - IF AMPLIFIER	Rev B			Ifcomponents.doc

Capacitors

33p	ceramic plate		C48,50

43p	ceramic plate		C6

47p	ceramic plate		C17,25,47

68p	ceramic plate		C52

75p	ceramic plate		C2

82p	ceramic plate		C20,28

100p	ceramic plate		C42,43

220p	ceramic plate		C18,26

270p	ceramic plate		C19,27

1n	multi layer ceramic	C21,36

4n7	multi layer ceramic	C41

10n	multi layer ceramic	C30

100n     mul i la er ceramic          c10,8

270n	multi layer ceramic	C11

1uF	Tantalum bead 25v	C31,33,54,55

10uF	Tantalum bead 25v	C32,34,35

1uF	Polyester		C44

4.7uF	Polyester		C1

Capacitors surface mount Y5V multi layer ceramic 50v

100n				C3,4,5,7,9,13,14,15,16,22,23,24,29,45,Cz2,3,4

Resistors 0.25w metal film 1% MF25 series

75R				R22

150R				R21

200R				R17,18,19

220R				R9,16,26,31,32,33

330R				R10

470R				R8

1K				R11,12,13,14,15,23,41,57

1k5                                              r62

2K7				R67

4K7				R46,61,66

4K99				R38

8K2				R59

10K				R58,64

12K				R49

27K				R40,48

33K				R27,28,29,30,34,35,36,37,54

47K				R56,60

68K				R63

82K				R20

100K				R42,43,44,45,50,51,52,55

180K				R39,47

4M7				R53

Resistors 1w metal film

47R				R24,25

Resistors surface mount 1205 0.063w

3K3				R65

Preset Potentiometers

1K	1 turn			R1

100R	22 turns		R2

20K	1 turn			R3

500K	22 turns		R4,5

500R	1 turn			R6

100K	1 turn			R7

Inductors

2.2uH	15 turns on Amidon L43-6		L1,2

47uH	Axial RFC				L3,7,8,9,10

4.7uH	Axial RFC				L11

36t on T37-6	(3.95uH)			L12

Pri 4 turns, sec 3.5 turns on BN61-202		T1

15 turns trifilar on Amidon L43-6

pri 2 windings, sec 1 winding 0.3mm		T2

Type 43 ferrite bead				FB1,2,3

Semi conductors

Integrated Circuits

AD600JN				U1,2

TL431ACLP			U3

- U4

- U5

TL084				U6,7,10,11

CA3046			U8,9

Diodes

BAV99				D0203,0607,0809,1011,1213,1617,1819

BAV70				D0405,1415,2021

Either				D1,22,25,26

8v2 Zener .25w			D23,24

Transistors and FET

J310				Q1

2N918	or similar		Q2

2N3904	or similar		Q3

BS170				Q4

Components off- board

100K lin pot			IF gain control

100K lin pot			Hang Time control

68K 0.25w resistor in series with 5v and IF gain pot

1mA 'S' meter and calibration resistors if required