TRANSMIT EXCITER BOARD  Rev B

Txexciter.doc

(Manual version)

The transmit exciter board amplifies the speech audio from the microphone and provides vox and anti-vox circuits. In addition, this module also contains 9001.5 and 8998.5 MHz crystal oscillators for upper and lower sideband BFOs, the transmitter balanced modulator and the receiver product detector.

Audio from the microphone is amplified by TR1, TR2 and associated components and is coupled by the MIC GAIN control to TR4. The output of this stage is coupled to pin 1 of the MC1496 balanced modulator. The BFO carrier signal is applied to pin 10. R45 is used to adjust the carrier balance for lowest output with no audio applied.

The output from the balanced modulator is taken from pin 6  and coupled to a buffer stage which is active in transmit only. The DSB signal is applied to the CW OSC board where a relay selects SSB or CW.

Microphone audio is also coupled to VOX buffer TR3 and detected by D5 and 6. The resulting DC voltage is amplified by U4A, the gain of which is set by the VOX GAIN control. VOX operation is disabled when pin 2 is taken to ground and this is effected by the I2C bus applied to U3, a  PCF8574.

Anti-vox from the speaker is connected to a detector consisting of D1 and D2. The DC output is amplified by U4B, the gain of which is set by the ANTI VOX control.

The Vox signal from U4A is applied to the inverting input of U4C and the anti-vox signal is applied to the non-inverting input. These signals are compared and when the vox signal is greater, the output of U4C is forced low. In the CW mode, a keyed voltage is applied to the inverting input to achieve the same effect.

The output of U4C is connected to the inverting input of U4D. Thus, when the output of U4C is low, the output of U4D goes high, providing a keying signal. Vox delay is established by C6 and the VOX DELAY control.

The output of U4D is applied to TR13, the output of which is connected to JP14 on the control board.

The BFO signal is also connected to MX1, the receiver product detector and mixed with the 9 MHz signal from the IF board to produce an audio output which is then fed to the AF amplifier.

There are no difficult adjustments. R45 should be adjusted to give the lowest output with no audio applied and this is best done with C21 lifted. Final adjustment should be done when the PA is working. The two crystal oscillators should be adjusted to the frequencies shown at first. Final adjustment is better left until the receiver is completed when they should be adjusted for most natural sounding audio.

COMPONENTS LIST - Transmit Exciter

Capacitors

5n	multi layer ceramic			C24,26

10n	multi layer ceramic			C9,12,22,27,28,29,42,76

50n	multi layer ceramic			C14

100n	multi layer ceramic			C1,34,36,38,39,41,44,49,72,53,52

220n	multi layer ceramic			C8,16,19,45

10p	ceramic plate				C31 (sot for 170mV p-p at pin 10, U6)

15p	ceramic plate				C50

56p	ceramic plate				C33,37

68p	ceramic plate				C13

100p	ceramic plate				C20,44,49

220p	ceramic plate				C30,43,47,48

470p	ceramic plate				C15

1uF 	tantalum bead 16v			C4,5,6,10,11,18,21,25

10uF	tantalum bead 16v			C7,17

22uF	tantalum bead 16v			C23,32

Capacitors, trimmers

5-65pF						C35,46,51

Resistors 0.25W metal film

- R19

- R80

- R70,65

- R33,44,57,68,85

- R81

- R29

220		R83,76

- R78,79

- R36,37,40,41

- R74

490		R54

- R3,54

- R55,58,75

- R38

1k		R5,21,26,43,48,16A

1k5		R32,60,71

2k2		R7,18,28,9,77,82

3k3		R16,50,51,61,73

4k7		R14

10k		R4,17,20,31,34,35,39,42,49,67,69

12k		R53

18k		R30

22k		R72

33k		R25

47k		R10

100k		R6,8,22,84

150k		R23

330k		R27

1M		R11

2M2		R12,24

6M8		R13

10 Turn preset pot

22k		R45

Semiconductors

Diodes

1N270		D1,2,3,4,5,6

1N4148	D9,7

Transistors

2N3904	TR1,2,3,4,5,11,12,13,14

2N918		TR9

Integrated circuits

MC1496	U6

MC3302	U4

PCF8574	U3

Inductors

Axial RFC 100uH		RFC1

Axial RFC 270uH		RFC2

T50-2 pri 10t sec 2t 0.4mm enam	T1,2

Relays

SPCO 5v OMRON G5V-1	RLY1

Mixers, DBM

SBL-1				MX1

Crystals

8998.5 kHz parallel resonant 30pF, HC18U		X1

9001.5 kHz parallel resonant 30pF, HC18U		X2

Connectors

IDC 10 pin			J1

SIL 8 pin header		J2

Potentiometers, panel mounting

3 - 10k log

1 - 3M lin